## Slide 1: Nuts and Bolts of Linux Socket Programming
Chun-Han Lin

## Slide 2: Outline
Mail Analogy
HTTP Example
IP address
Port
Communication Protocol
Socket
Echo Server and Client

## Slide 3: Mail Analogy
媽！！我沒錢了，
快匯錢給我！！！！
台北市○○區○○路○○號
黃 ○ ○ 女士 收
新竹市大學路1001號工程三館622室
林○○
Destination
IP Address
Destination
Port
Source
IP Address
Source
Port
Protocol

## Slide 4: HTTP Example
GET /index.html
www.nctu.edu.tw
80
140.113.210.234
55481
Destination
IP Address
Destination
Port
Source
IP Address
Source
Port
Protocol
140.113.60.211

## Slide 5: IP Address
An IP address is a numerical label assigned to each device participating in a computer network
  Host identification
  Location addressing
IP addresses are binary numbers
  IPv4 : 32-bit
    74.125.31.103
  IPv6 : 128-bit
    2404:6800:4008:c01::93

## Slide 6: Port
A port is an application-specific software construct serving as a communications endpoints in a computer’s host operating system
A port number is a 16-bit number
  20 : FTP data transfer
  21 : FTP control
  23 : Telnet
  53 : Domain Name System
  80 : HTTP
  etc…

## Slide 7: Communication Protocol
A communication protocol is a system of digital rules for message exchange between computers

## Slide 8: Socket
Network socket
  An endpoint of an inter-process communication flow across a computer network
Socket API
  Allows application programs to control and use network sockets
  By using socket API, programmers can focus on the design of their application instead of how to transfer data over the network

## Slide 9: Echo Server - Overview
Create socket
Initialize
sockaddr
bind
listen
accept
recv
send

## Slide 10: Echo Server – Create Socket
int socket(int domain, int type, int protocol)
  In sys/socket.h
  Arguments
    Domain
      AF_INET : The IPv4 address family
    Type
      SOCK_STREAM : TCP
    Protocol
      0 : Auto
  Return
    Success : The socket ID
    Fail : -1

## Slide 11: Echo Server – Initialize sockaddr
Structure member
  sin_family
    AF_INET : The IPv4 address family
  sin_addr.s_addr
    INADDR_ANY : All interfaces
  sin_port
    Port number
      htons
        Convert a short from host to TCP/IP network byte order
        In netinet/in.h

## Slide 12: Echo Server - bind
Associates a socket with a local endpoint
int bind(int socketfd, struct sockaddr * addr, size_t addr_len)
  In sys/socket.h
  Arguments
    socketfd : The socket
    addr : A pointer which points to the sockaddr_in
    addr_len : The length of sockaddr_in
  Return
    Success : 0
    Fail : -1

## Slide 13: Echo Server - listen
Set the socket to listening socket, and inform the OS that the socket is ready for accepting incoming connections
int listen(int socketfd, int backlog)
  In sys/socket.h
  Arguments
    socketfd : The socket
    backlog : The maximum rate at which the server can accept new TCP connections
  Return
    Success : 0
    Fail : -1

## Slide 14: Echo Server - accept
Accept the request of the incoming connection
int accept(int socketfd, struct sockaddr * addr, size_t addrlen)
  In sys/socket.h
  Arguments
    socketfd : The socket
    addr : A pointer points to the sockaddr_in which stores the IP address of the client
    addrlen : The length of sockaddr_in
  Return
    Success : The socket ID of the client
    Fail : -1

## Slide 15: Echo Server - recv
Receive data from socket
int recv(int socket, void *buf, int len, unsigned int flag)
  In sys/socket.h
  Arguments
    socket : The socket
    buf : A pointer which points to the buffer for the incoming data
    len : The maximum length of receiving data
    flag : 0
  Return
    Success : The length of received data
    Fail : -1

## Slide 16: Echo Server - send
Send data through socket
int send(int socket, void *msg, int len, unsigned int flags)
  In sys/socket.h
  Arguments
    socket : the socket
    msg : A pointer which points to the buffer
    len : The maximum length of outgoing data
    flags : 0
  Return
    Success : The length of transmitted data
    Fail : -1

## Slide 17: Echo Client - Overview
Create socket
Initialize
sockaddr
connect
send
recv

## Slide 18: Echo Client – Initialize sockaddr
Structure member
  sin_family
    AF_INET : The IPv4 address family
  sin_addr.s_addr
    IP address of the server
      inet_addr
        Convert string of IP address to 32-bit unsigned integer
        In netinet/in.h, arpa/inet.h
  sin_port
    Port number
      htons
        Convert a short from host to TCP/IP network byte order
        In netinet/in.h

## Slide 19: Echo Client - connect
Establish connection between client and server
int connect(int sockfd, struct sockaddr *addr, int addrlen)
  In sys/socket.h
  Arguments
    sockfd : The socket
    addr : A pointer points to the sockaddr_in which stores the IP address and port number of the server
    addrlen : The length of sockaddr_in
  Return
    Success : 0
    Fail : -1

## Slide 20: Q & A